## Slide 1
Digital I/O Voltage Level
Standards
Hamza Solmaz
01.08.2025
MEOS ETM

## Slide 2
What are ideal conditions?
Reliability
Low cost
Low power consumption
High speed
Supply voltage range

## Slide 3
TTL
CMOS
LVDS
LVPECL
Others
Comparison
Conclusion
OUTLINE

## Slide 4
TTL
Operates with 5V
10 ns propagation delay
10 mW steady power consumption
Up to 10 Mbps
Sub-types
Low-power TTL (33ns, 1mW)
High Speed TTL (6ns, 22 mW)
Schottky TTL (3ns, 19mW)
Low-power Schottky TTL (9.5ns, 2mW)
Applications
UART
Figure 1 I/O Voltage Levels of TTL

## Slide 5
CMOS
Supply voltage may vary between 1.8V-15V
Noise margin is higher than TTL
Speed is higher than TTL
Frequency dependent power consumption
Subtypes
LVCMOS
Advanced CMOS
Bipolar CMOS
HCMOS
Applications
I2C
SPI
(All about circuits)
Figure 2: Voltage levels of CMOS

## Slide 6
LVDS
Differential data transmission
2.4V-3.3V supply voltage
1.2V common mode voltage
0.4V swing
Consumes constant current (3.5mA)
Lower EMI effect
Low power consumption (8.75mW)
Maximum 4Gbps speed per lane
Sub-Types
Bus LVDS (Multiple reciever)
SLVS (800 mV supply)
Mini-LVDS
Applications
Flat Panel Display Link
Gigabit Multimedia Serial Link
Figure 3: LVDS termination circuit schematic
(Renesas)

## Slide 7
LVPECL
Derived from ECL and PECL
Differential pair
3.3V supply voltage
Vcc-2V common mode voltage
800mV voltage swing
Up to 10 Gbps
Higher power consumption than LVDS
Low noise tolerant
Application
Gigabit Ethernet
Fiber Channel
Optical Communication
Figure 4: LVPECL Y-termination circuit schematic
(Renesas)

## Slide 8
Others
HCSL
PCIe reference clock
Low phase jitter
100 MHz
SSTL
Uses a reference voltage (VDD/2)
Swing around Vref
DDR SDRAM
HSTL
Signaling between ICs
0V-1.5V signaling range
Single-ended or differential
Beyond 180 MHz

## Slide 9
COMPARISON
Standard | Supply Voltage | Signal Type | Speed | Power Consumption | Cost and Complexity
TTL | 5V | Single-ended | <10 Mbps | 10 mW | Low
CMOS | 1.8V-15V | Single-ended | Depend on MOS characteristics | Depend on switching frequency | Low-medium
LVDS | 2.4V-3.3V | Differential | < 4 Gbps | 8.75 mW | Medium
LVPECL | 3.3V or 2.5V | Differential | <10 Gbps | 50-100 mW | High

## Slide 10
Is it possible to communicate
with different logic levels?
Converters
Basic resistive voltage dividers
Level shifters or level translators (TXS0102)
FPGA or Microcontrollers (STM32)
Differences
Single-ended / Differential
Voltage Levels
Speed

## Slide 11
CONCLUSION

## Slide 12
THANKS FOR LISTENING

## Slide 13
Q&A
TTL
https://www.techtarget.com/whatis/definition/transistor-to-transistor-logic-TTL
CMOS
https://www.nxp.com/docs/en/user-guide/UM10204.pdf
https://www.allaboutcircuits.com/textbook/digital/chpt-3/logic-signal-voltage-levels
LVDS
https://www.ti.com/lit/an/snla165/snla165.pdf?ts=1753844644513
https://resources.pcb.cadence.com/blog/2023-lvds-signals-crashcourse
LVPECL
https://www.renesas.com/en/document/apn/lvds-pecl-termination-app-note
https://www.ti.com/lit/an/slla120/slla120.pdf
https://www.rfwireless-world.com/terminology/ecl-vs-pecl-vs-lvpecl
General Information
https://ww1.microchip.com/downloads/aemDocuments/documents/VOP/ApplicationNotes/ApplicationNotes/Signal+Types+and+Terminations.pdf
References